##### Batch Production of Amino Acids

##### Introduction

This design involves the batch production of amino acids.  The four amino acids being produced are L-aspartic acid, L-phenylalanine, L-lysine HCl, and L-leucine.  These amino acids are primarily used as dietary supplements.  However, L-aspartic acid and L-phenylalanine are the two main ingredients in the artificial sweetener aspartame.

Capstone Chemical Corporation requested the most profitable method(s) for producing the following amounts of the amino acids:

- 1% of the world market of L-lysine HCl

- 2.5% of the world market of L-leucine

- 2.5% of the world market of L-aspartic acid

- 2.5% of the world market of L-phenylalanine

The amino acid facility was designed to produce L-lysine and L-leucine (in the amounts shown above) in alternating campaigns throughout the year.  However, the facility was also to have the capability to produce L-aspartic acid and L-phenylalanine, if the market fluctuates or if a potential buyer requests an immediate production of these two amino acids.  The final design includes raw material needs, equipment schematics, equipment bare module costs, utilities needed for the process, waste treatment cost, a 5-year Monte Carlo Simulation using a 5-year MACRS Depreciation Method detailing payback periods, and net present value information for the proposed amino acid batch facility.  In addition, a 3-dimensional drawing detailing the reactor design and a plot plan illustrating the plant layouts have been generated.

##### Results

Amino Acid Process Descriptions

Figure 1 is the process flow diagram for the amino acid facility corresponding to the stream tables given in Tables 1, 2, 3, 4.  This figure and these stream tables represent only 1 of 19 reactors needed for the amino acid facility.  The remaining reactors follow the same schematics with few exceptions, as discussed below.

Table 1: Stream Tables for Leucine

| Stream | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 30 | 30 | 30 | 30 |
| Pressure (bar) | 1 | 1 | 1 | 1 |
| Vapor mole fraction | 0 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 50 | 50 | 175,000 | 175,000 |
| Flowrate (m3/batch) | 0.05 | 0.05 | 174.95 | 174.95 |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 45 | 45 | 175,000 | 175,000 |
| Biomass (kg/batch) | 5 | 5 | 0 | 0 |
| Eluting Water (kg/batch) | 0 | 0 | 0 | 0 |
| L-leucine (kg/batch) | 0 | 0 | 0 | 0 |

| Stream | 13 | 14 | 15 | 16 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 30 | 30 | 30 | 30 |
| Pressure (bar) | 1 | 1 | 1 | 1 |
| Vapor mole fraction | 0 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 175,000 | 17,500 | 157,500 | 157,500 |
| Flowrate (m3/batch) | 175 | - | 175 | 175 |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 154,000 | 0 | 154,000 | 154,000 |
| Biomass (kg/batch) | 17,500 | 17,500 | 0 | 0 |
| Eluting Water (kg/batch) | 0 | 0 | 0 | 0 |
| L-leucine (kg/batch) | 3,500 | 0 | 3,500 | 3,500 |

| Stream | 17 | 18 | 19 | 20 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 70 | 30 | 70 | 70 |
| Pressure (bar) | 1 | 1 | 1 | 1 |
| Vapor mole fraction | 0 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 97,800 | 154,000 | 101,300 | 185,300 |
| Flowrate (m3/batch) | 175 | 175 | 175 | 175 |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 0 | 154,000 | 0 | 0 |
| Biomass (kg/batch) | 0 | 0 | 0 | 0 |
| Eluting Water (kg/batch) | 97,800 | 0 | 97,800 | 178,400 |
| L-leucine (kg/batch) | 0 | 0 | 3,500 | 6,900 |

| Stream | 21 | 22 | 23 | 24 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 100 | 25 | 100 | 100 |
| Pressure (bar) | 1 | 1 | 1 | 1 |
| Vapor mole fraction | 1 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 96,700 | 96,700 | 170,200 | 170,200 |
| Flowrate (m3/batch) |  |  |  |  |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 0 | 0 | 0 | 0 |
| Biomass (kg/batch) | 0 | 0 | 0 | 0 |
| Eluting Water (kg/batch) | 96,700 | 96,700 | 163,400 | 163,400 |
| L-leucine (kg/batch) | 0 | 0 | 6,800 | 6,800 |

| Stream | 25 | 26 | 27 | 28 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 100 | 100 | 100 | 100 |
| Pressure (bar) | 1 | 1 | 1 | 1 |
| Vapor mole fraction | 0 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 170,200 | 88,500 | 4,500 | 84,000 |
| Flowrate (m3/batch) |  |  |  |  |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 0 | 0 | 0 | 0 |
| Biomass (kg/batch) | 0 | 0 | 0 | 0 |
| Eluting Water (kg/batch) | 163,400 | 81,700 | 1100 | 80,600 |
| L-leucine (kg/batch) | 6,800 | 3,400 | 0 | 3,400 |
| L-leucine (solid) (kg/batch) | 0 | 3,400 | 3,400 | 0 |

Table 2: Stream Tables for Lysine

| Stream | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 30 | 30 | 30 | 30 |
| Pressure (bar) | 1 | 1 | 1 | 1 |
| Vapor mole fraction | 0 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 50 | 50 | 175,000 | 175,000 |
| Flowrate (m3/batch) | 0.05 | 0.05 | 174.95 | 174.95 |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 45 | 45 | 175,000 | 175,000 |
| Biomass (kg/batch) | 5 | 5 | 0 | 0 |
| Eluting Water (kg/batch) | 0 | 0 | 0 | 0 |
| L- lysine (kg/batch) | 0 | 0 | 0 | 0 |

| Stream | 13 | 14 | 15 | 16 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 30 | 30 | 30 | 30 |
| Pressure (bar) | 1 | 1 | 1 | 1 |
| Vapor mole fraction | 0 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 175,000 | 17,500 | 157,500 | 157,500 |
| Flowrate (m3/batch) | 175 | - | 175 | 175 |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 142,555 | 0 | 142,555 | 142,555 |
| Biomass (kg/batch) | 17,500 | 17,500 | 0 | 0 |
| Eluting Water (kg/batch) | 0 | 0 | 0 | 0 |
| L- lysine (kg/batch) | 14,945 | 0 | 14,945 | 14,945 |

| Stream | 17 | 18 | 19 | 20 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 70 | 30 | 70 | 70 |
| Pressure (bar) | 1 | 1 | 1 | 1 |
| Vapor mole fraction | 0 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 175,000 | 142,555 | 29,600 | 58,600 |
| Flowrate (m3/batch) | 175 | 175 | 175 |  |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 0 | 142,555 | 0 | 0 |
| Biomass (kg/batch) | 0 | 0 | 0 | 0 |
| Eluting Water (kg/batch) | 175,000 | 0 | 12,200 | 27,400 |
| L- lysine (kg/batch) | 0 | 0 | 17,400 | 31,200 |

| Stream | 21 | 22 | 23 | 24 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 100 | 25 | 100 | 100 |
| Pressure (bar) | 1 | 1 | 1 | 1 |
| Vapor mole fraction | 1 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 7,500 | 7,500 | 68,800 | 68,800 |
| Flowrate (m3/batch) |  |  |  |  |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 0 | 0 | 0 | 0 |
| Biomass (kg/batch) | 0 | 0 | 0 | 0 |
| Eluting Water (kg/batch) | 7,500 | 7,500 | 36,000 | 36,000 |
| L- lysine (kg/batch) | 0 | 0 | 32,800 | 32,800 |

| Stream | 25 | 26 | 27 | 28 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 100 | 100 | 100 | 80 |
| Pressure (bar) | 2 | 1 | 1 | 1 |
| Vapor mole fraction | 0 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 68,800 | 50,800 | 19,300 | 29,000 |
| Flowrate (m3/batch) |  |  |  |  |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 0 | 0 | 0 | 0 |
| Biomass (kg/batch) | 0 | 0 | 0 | 0 |
| Eluting Water (kg/batch) | 36,000 | 18,000 | 2,900 | 15,200 |
| L-lysine (kg/batch) | 32,800 | 16,400 | 2,600 | 13,800 |
| L- lysine (solid) (kg/batch) | 0 | 16,400 | 16,400 | 0 |

Table 3: Stream Tables for Aspartic Acid

| Stream | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 30 | 30 | 30 | 30 |
| Pressure (bar) | 1 | 1 | 1 | 1 |
| Vapor mole fraction | 0 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 50 | 50 | 175,000 | 175,000 |
| Flowrate (m3/batch) | 0.05 | 0.05 | 174.95 | 174.95 |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 45 | 45 | 175,000 | 175,000 |
| Biomass (kg/batch) | 5 | 5 | 0 | 0 |
| Eluting Water (kg/batch) | 0 | 0 | 0 | 0 |
| L- aspartic acid (kg/batch) | 0 | 0 | 0 | 0 |

| Stream | 13 | 14 | 15 | 16 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 30 | 30 | 30 | 30 |
| Pressure (bar) | 1 | 1 | 1 | 1 |
| Vapor mole fraction | 0 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 175,000 | 17,500 | 157,500 | 157,500 |
| Flowrate (m3/batch) | 175 | - | 175 | 175 |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 138,880 | 0 | 138,880 | 138,880 |
| Biomass (kg/batch) | 17,500 | 17,500 | 0 | 0 |
| Eluting Water (kg/batch) | 0 | 0 | 0 | 0 |
| L- aspartic acid (kg/batch) | 18,620 | 0 | 18,620 | 18,620 |

| Stream | 17 | 18 | 19 | 20 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 70 | 30 | 70 | 70 |
| Pressure (bar) | 1 | 1 | 1 | 1 |
| Vapor mole fraction | 0 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 175,000 | 138,880 | 193,620 | 310,460 |
| Flowrate (m3/batch) | 175 | 175 | 175 |  |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 0 | 138,880 | 0 | 0 |
| Biomass (kg/batch) | 0 | 0 | 0 | 0 |
| Eluting Water (kg/batch) | 175,000 | 0 | 175,000 | 273,220 |
| L- aspartic acid (kg/batch) | 0 | 0 | 18,620 | 37,240 |

| Stream | 21 | 22 | 23 | 24 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 100 | 25 | 100 | 100 |
| Pressure (bar) | 1 | 1 | 1 | 1 |
| Vapor mole fraction | 1 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 70,600 | 70,600 | 246,040 | 246,040 |
| Flowrate (m3/batch) |  |  |  |  |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 0 | 0 | 0 | 0 |
| Biomass (kg/batch) | 0 | 0 | 0 | 0 |
| Eluting Water (kg/batch) | 70,600 | 70,600 | 208,800 | 208,800 |
| L- aspartic acid (kg/batch) | 0 | 0 | 37,240 | 37,240 |

| Stream | 25 | 26 | 27 | 28 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 100 | 100 | 100 | 100 |
| Pressure (bar) | 2 | 1 | 1 | 1 |
| Vapor mole fraction | 0 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 246,040 | 141,640 | 24,800 | 116,840 |
| Flowrate (m3/batch) |  |  |  |  |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 0 | 0 | 0 | 0 |
| Biomass (kg/batch) | 0 | 0 | 0 | 0 |
| Eluting Water (kg/batch) | 208,800 | 104,400 | 6,180 | 98,220 |
| L- aspartic acid (kg/batch) | 37,240 | 18,620 | 0 | 18,620 |
| L-aspartic acid (solid) (kg/batch) |  | 18,620 | 18,620 | 0 |

Table 4: Stream Tables for Phenylalanine

| Stream | 1 | 2 | 3 | 4 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 30 | 30 | 30 | 30 |
| Pressure (bar) | 1 | 1 | 1 | 1 |
| Vapor mole fraction | 0 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 50 | 50 | 175,000 | 175,000 |
| Flowrate (m3/batch) | 0.05 | 0.05 | 174.95 | 174.95 |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 45 | 45 | 175,000 | 175,000 |
| Biomass (kg/batch) | 5 | 5 | 0 | 0 |
| Eluting Water (kg/batch) | 0 | 0 | 0 | 0 |
| L-phenylalanine (kg/batch) | 0 | 0 | 0 | 0 |

| Stream | 13 | 14 | 15 | 16 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 30 | 30 | 30 | 30 |
| Pressure (bar) | 1 | 1 | 1 | 1 |
| Vapor mole fraction | 0 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 175,000 | 17,500 | 157,500 | 157,500 |
| Flowrate (m3/batch) | 175 | - | 175 | 175 |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 153,702 | 0 | 153,702 | 153,702 |
| Biomass (kg/batch) | 17,500 | 17,500 | 0 | 0 |
| Eluting Water (kg/batch) | 0 | 0 | 0 | 0 |
| L-phenylalanine (kg/batch) | 3,798 | 0 | 3,798 | 3,798 |

| Stream | 17 | 18 | 19 | 20 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 70 | 30 | 70 | 70 |
| Pressure (bar) | 1 | 1 | 1 | 1 |
| Vapor mole fraction | 0 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 69,000 | 153,702 | 72,800 | 110,600 |
| Flowrate (m3/batch) | 175 | 175 | 175 |  |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 0 | 153,702 | 0 | 0 |
| Biomass (kg/batch) | 0 | 0 | 0 | 0 |
| Eluting Water (kg/batch) | 69,000 | 0 | 69,000 | 102,900 |
| L-phenylalanine (kg/batch) | 0 | 0 | 3,800 | 7,700 |

| Stream | 21 | 22 | 23 | 24 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 100 | 25 | 100 | 100 |
| Pressure (bar) | 1 | 1 | 1 | 1 |
| Vapor mole fraction | 1 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 67,700 | 67,700 | 86,600 | 86,600 |
| Flowrate (m3/batch) |  |  |  |  |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 0 | 0 | 0 | 0 |
| Biomass (kg/batch) | 0 | 0 | 0 | 0 |
| Eluting Water (kg/batch) | 67,700 | 67,700 | 78,600 | 78,600 |
| L-phenylalanine (kg/batch) | 0 | 0 | 8,000 | 8,000 |

| Stream | 25 | 26 | 27 | 28 |
| --- | --- | --- | --- | --- |
| Temp ((C) | 100 | 100 | 100 | 100 |
| Pressure (bar) | 2 | 1 | 1 | 1 |
| Vapor mole fraction | 0 | 0 | 0 | 0 |
| Flowrate (kg/batch) | 86,600 | 47,100 | 9,300 | 37,800 |
| Flowrate (m3/batch) |  |  |  |  |
| Component Flowrates |  |  |  |  |
| Nutrient Media (kg/batch) | 0 | 0 | 0 | 0 |
| Biomass (kg/batch) | 0 | 0 | 0 | 0 |
| Eluting Water (kg/batch) | 78,600 | 39,300 | 5,400 | 33,900 |
| L-phenylalanine (kg/batch) | 8,000 | 4,000 | 100 | 3,900 |
| L-phenylalanine (solid) (kg/batch) | 0 | 3,800 | 3,800 | 0 |

Reactors, R-501-519, operate in parallel.  The kinetic data for the reactions can be found in References 1-4.  The reactor effluent is then pumped to a series of rotary drum precoat filters.  Here, the bacteria are filtered out of the slurry.  The bacteria-free slurry is then sent to storage vessels, V-501-519.  From the storage vessels, the slurry is pumped to ion exchange towers, T-501-516, where the amino acid is removed using an ion exchange resin.  One resin, Dowex Marathon C, was chosen for use in the process.  It is important to note that L-aspartic acid bypasses this section of the process, since it is crystallized in solution through precipitation.  The ion exchange slurry is then sent to crystallizers CR-501-520.  In this section, the amino acid is crystallized, using a series of Draft Tube Baffle (DTB) Crystallizers, precipitated out of solution, and filtered out of the slurry using rotary drum filters F-506-510.  The amino acid product is then sent to the product storage area of the facility.

This amino acid facility is the most profitable design for producing at least 1% of the world market of L-lysine and 2.5% of the world market of L-leucine with the flexibility to produce approximately 2.5% of the world market of L-aspartic acid and L-phenylalanine upon demand.  Table 5 shows the batch and process information for this facility.

Table 5:	 Batch and Process Information for the Amino Acid Facility

Design Economics & Reactor Scheduling

The reactor schedule for the amino acid reactors is shown in Figure 2.  This figure represents a recurring 14-day cycle, showing the schedule needed for all processes using all 19 reactors to produce either L-leucine and L-lysine or L-aspartic acid and L-phenylalanine.  Figure 3 illustrates the 14-day separation schedule for the amino acid facility.  The separation schedule was based upon the 14-day reactor schedule shown in Figure 2.  There are four batches per cycle in the L-leucine and L-phenylalanine processes, seven for L-lysine, and nine for L-aspartic acid.

For the case when L-leucine and L-lysine are being produced, one of the reactors (R-517) in the L-leucine process does not operate for the entire year and has the schedule shown in Table 6.  R-517 produces the last of the L-leucine and L-lysine in approximately 5700 hours and is idle for the remainder of the year.  For the case when L-phenylalanine and L-aspartic acid are being produced, it is important to note that R-517 will produce L-phenylalanine all year as shown in Figure 2.

| Schedule A |  | Day 1 | Day 2 | Day 3 | Day 4 | Day 5 | Day 6 | Day 7 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | D | N | G | D | N | G | D | N | G | D | N | G | D | N | G | D | N | G | D | N | G |
| Ion Exchange 1 | R | C |  | F | E |  | R | C |  | F | E |  | R | C |  | F | E |  | R | C |  | F | E |  | R | C |  | F | E |  | R | C |  | F | E |  | R | C |  | F | E |  |  |
| Ion Exchange 2 | E | R | C |  | F |  | E | R | C |  | F |  | E | R | C |  | F |  | E | R | C |  | F |  | E | R | C |  | F |  | E | R | C |  | F |  | E | R | C |  | F |  |  |
| Crystallizer 1 |  | O | C |  | USS | O | C |  | USS | O | C |  | USS | O | C |  | USS | O | C |  | USS | O | C |  | USS | O | C |  | USS |  |
| Crystallizer 2 | USS | O | C |  | USS | O | C |  | USS | O | C |  | USS | O | C |  | USS | O | C |  | USS | O | C |  | USS | O | C |  |  |
| Crystal Filter |  | O | C | O | C |  |  | O | C | O | C |  |  | O | C | O | C |  |  | O | C | O | C |  |  | O | C | O | C |  |  | O | C | O | C |  |  | O | C | O | C |  |  |
| Schedule B | M | E | G | M | E | G | M | E | G | M | E | G | M | E | G | M | E | G | M | E | G |  |
|  | Day 1 | Day 2 | Day 3 | Day 4 | Day 5 | Day 6 | Day 7 |  |
| Schedule A |  | Day 8 | Day 9 | Day 10 | Day 11 | Day 12 | Day 13 | Day 14 |
|  |  | D | N | G | D | N | G | D | N | G | D | N | G | D | N | G | D | N | G | D | N | G |
| Ion Exchange 1 | R | C |  | F | E |  | R | C |  | F | E |  | R | C |  | F | E |  | R | C |  | F | E |  | R | C |  | F | E |  | R | C |  | F | E |  | R | C |  | F | E |  |  |
| Ion Exchange 2 | E | R | C |  | F |  | E | R | C |  | F |  | E | R | C |  | F |  | E | R | C |  | F |  | E | R | C |  | F |  | E | R | C |  | F |  | E | R | C |  | F |  |  |
| Crystallizer 1 |  | O | C |  | USS | O | C |  | USS | O | C |  | USS | O | C |  | USS | O | C |  | USS | O | C |  | USS | O | C |  | USS |  |
| Crystallizer 2 | USS | O | C |  | USS | O | C |  | USS | O | C |  | USS | O | C |  | USS | O | C |  | USS | O | C |  | USS | O | C |  |  |
| Crystal Filter |  | O | C | O | C |  |  | O | C | O | C |  |  | O | C | O | C |  |  | O | C | O | C |  |  | O | C | O | C |  |  | O | C | O | C |  |  | O | C | O | C |  |  |
| Schedule B | M | E | G | M | E | G | M | E | G | M | E | G | M | E | G | M | E | G | M | E | G |  |
|  | Day 8 | Day 9 | Day 10 | Day 11 | Day 12 | Day 13 | Day 14 |  |
| Schedule A | Day Shift | 8 AM to 4 PM |  |  |  |  |  |  |  |  | F |  | Feeding Ion Exchange Column |  |  |  |
|  | Night Shift | 4 PM to Midnight |  |  |  |  |  |  |  |  | E |  | Eluting Ion Exchange Column |  |  |  |  |
|  | Graveyard A | Midnight to 8 AM |  |  |  |  |  |  |  |  |  |  |  |  | R |  | Regenerating Ion Exchange Column |  |  |
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | C |  | Cleaning Equipment |  |  |  |  |  |  |  |
| Schedule B | Morning Shift | 4 AM to Noon |  |  |  |  |  |  |  |  | USS |  | Operating at Unsteady State |  |  |  |  |
|  | Evening Shift | Noon to 8 PM |  |  |  |  |  |  |  |  | O |  | Operating at Steady State |  |  |  |  |  |
|  | Graveyard B | 8 PM to 4 AM |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |

Table 6: Processing Time for Reactor-517 in L-leucine/L-lysine Process

The break-even prices for the L-leucine and L-lysine processes are $13.30/kg and $2.70/kg, respectively.  Figure 4 shows the yearly operating cost breakdown for these processes.  Raw materials represent the largest cost followed by waste treatment and utility costs.  A breakdown of the raw material cost for the L-leucine and L-lysine processes is shown in Figure 5.  Figure 6 illustrates the equipment cost breakdown, and Figure 7 details the utility cost breakdown for these processes.

Figure 4:  Yearly Operating Cost Breakdown for L-leucine and L-lysine

Figure 5:  Raw Material Cost Breakdown for L-leucine and L-lysine

Figure 6:  Total Equipment Cost Breakdown for L-leucine and L-lysine

## Figure 7:  Total Utility Cost Breakdown for L-leucine and L-lysine

In order to run the L-phenylalanine and L-aspartic acid processes, additional equipment, not shown in Figure 1, must be purchased and is listed in Table 7.

Table 7:  Additional Equipment Needed for L-phenylalanine and L-aspartic acid

| L-aspartic Acid Process |  |  |
| --- | --- | --- |
| Equipment Type | Number Required | Specifications |
| Heat Exchangers | 2 | 412 m2 |
| Centrifugal Pumps | 8 | 2 kW |
| Crystal Filter | 4 | 1.4 m2 |
| L-phenylalanine Process |  |  |
| Equipment Type | Number Required | Specifications |
| Heat Exchangers | 2 | 345 m2 |

The break-even prices for the L-phenylalanine and L-aspartic acid processes are $15.00/kg and $12.00/kg, respectively.  Figure 8 represents the yearly operating cost breakdown for these processes.  A breakdown of raw material cost for the processes is shown in Figure 9.  Figure 10 is the equipment cost breakdown, and Figure 11 details the utility cost breakdown for these processes.

Figure 8:  Yearly Operating Cost Breakdown for L-aspartic acid & L-phenylalanine

Figure 9:  Raw Material Cost Breakdown for L-aspartic acid & L-phenylalanine

Figure 10: Total Equipment Cost Breakdown for L-aspartic acid & L-phenylalanine

Figure 11: Total Utility Cost Breakdown for L-aspartic acid & L-phenylalanine

Conclusions & Recommendations

In conclusion, Technocats, Inc., has completed the final design for the requested amino acid facility as shown in Figure 1.  Technocats, Inc., has determined equipment needed to produce L-lysine and L-leucine, as well as, additional equipment needed to produce L-phenylalanine and L-aspartic acid if the market fluctuated to do so or if a potential buyer offered an outstanding premium to produce the two.  This provides Capstone Chemical Corporation with the flexibility to produce any of the four amino acids discussed above.

Another item addressed during the design process was the issue of scheduling.  Scheduling was used to determine how each amino acid would “travel” through the process.  A full 14-day reactor schedule was formulated to fit the 8-hour work shifts.  A full 14-day schedule for the separations section was also developed and designed to fit the 8-hour work shifts.  These schedules are how the batch amino acid facility will operate.  The schedules are illustrated in Figures 2 and 3.

Technocats, Inc., strongly recommends the construction of the proposed batch facility.  The amino acid facility will produce L-lysine, L-leucine, L-phenylalanine, and L-aspartic acid utilizing the same equipment.  This provides Capstone Chemical Corporation with the flexibility to produce multiple products and shift from product to product, as the market fluctuates.  The break-even and market prices for all four amino acids are summarized in Table 8.

Table 8:  Amino Acid Break-Even Prices

| Amino Acid | Break-even Price ($/kg) | Market Price ($/kg)*** |
| --- | --- | --- |
| L-lysine HCl | 2.70 | 4.75 |
| L-leucine | 13.30 | 140.00 |
| L-aspartic acid | 12.00 | 20.00 |
| L-phenylalanine | 15.00 | 84.00 |

***all prices are quoted from Chemical Market Reporter (March 2003)

##### A detailed economic analysis including bare module costs and a 5-year Monte Carlo simulation is given in the Appendicies.  The significance of this simulation is that the probability of losing money is virtually zero for the amino acids process.  Detailed calculations of all equipment, cleaning times, and impeller power can also be found in the Appendicies.  Finally, a reactor HAZOP, a plant plot plan, and PDMS drawings of reactors can also be found in the Appendix.

##### References

- Takamatsh, T., K. Yamashita, and A. Sumi, “Kinetics of Production of L-aspartic Acid by Aspartase of Immobilized Eschericia Coli Cells,” Japanese Journal of Fermentation Technology, Vol 58, No. 2, pp.129-33, 1980.

- Tsuchida, Takayasu and Koji Kubota, et. al.  “Production of L-Phenylalanine by a Mutant of Brevibacterium lactofermentum 2256,” Agricultural Biological Chemistry, Vol. 51, No. 8, pp. 2095-2101, 1987.

- (Rule of Thumb) http://www.glue.umd.edu/~nsw/ench485/lab9c.htm.

- Tada, Kiyoshi, Michimasa Kishimoto, Takeshi Omasa, Yoshio Katakura, and Ken-Ichi Suga, "Constrained Optimization of L-lysine Production Based on Metabolic Flux Using a Mathematical Programming Method," Journal of Bioscience and Bioengineering, Vol. 91, No. 4, pp. 344-351, 2001.

# Text boxes

Figure 3: Separation Scheduling for the Amino Acid Process

Figure 2: Reactor Scheduling for the Amino Acid Process